## Slide 1: (Liquid) Cocoa Butter Production Flow Keymar Warehouse-Riverside, NJ
Receiving of containers
Boxes examined and Palletized
Pallets moved to warehouse Storage in Warehouse
Ambient Temperature
Boxes picked and staged
Boxes opened plastic removed
Melter
Coils 220 F , Liquid temperature 120 F
25 micron filter
Hot holding tank
120 F – 140 F
10 micron filter—CCP1
Magnet CP
Tanker filled
Tanker sealed
Shipping Product
Delivery order w/ Seal # and country of origin
Receiving Delivery Order
Receiving-Daily inbounds
Return of Liquid
Hold for evaluation
Upon disposition, return to melter, for melted, dedorizing side for deodorized, or destroy.
Destroy
11/4” wire mesh screen
1/8” wire mesh screen
Check for Quantity and Damage
Damaged boxes identified and labeled on location tag.
Good boxes identified and labeled on location tag
Product sample taken sent to potential buyers
Customer approval received and delivery order released
Retain sample collected
Seal Sheet
Warehouse receipt
Sample Log
(1) 25 uFilter Log-inbound
Holding Tank Temperature Log
Magnet check daily
(3) 10 u Filter CCP1 Log outbound
Outbound BOL Wash Tag, Seal #
Pre shipment Review Log. Riverside Lqd Outbound Proc.
Shipping Log (Customer Traceability) – Liquid Load Database.
Warehouse Inventory Log
(paper and electronic database)
Automatic Inventory Adjustment
Reviewed as stated in review document
Colored blocks indicate flow , supporting information no fill.
Check Tankard seals, washout certificate, top load certificate check hose prio and post loading
For deodorized butter see attached flow to be inserted following this step, all process below to remain.
Pallet checked
Butter to be melted
Butter to be delivered in block form. Cargo owner designates destination, quantity to move, carrier and pick up date. Keymar to create BOL
Cargo verified by
Pick up number
Provided by
Cargo owner.
Trailer checked for
cleanliness,
Integrity of
Trailer sign off
Once loaded.
Sealed and
Seals recorded.
Signed by trucker
And loader.

## Slide 2: LIQUID COCOA BUTTER TO DEODORIZED BUTTER. ADDENDUM TO PRODUCTION FLOW KEYMAR WAREHOUSE COMPANY, INC. RIVERSIDE NJ
Hot holding tank
120 F – 140 F
Blend based on values of
FFA, IV and Moisture
from holding tanks, sent to
Feed tanks.
Feed tanks to deodorizer.
Deodorized butter to finished tank
Finish tank 140 F +/- 10 F
Finished tank to filter CCP
Finished tank to truck through magnet, continue flow from page 1
Quality checks performed every 2 hours +/- 15 minutes. Documented, 50 micron filter exiting deodorizer.
Flow meter, 50 micron filter
Flow meter
Flow meter and 10 micron filter
All liquid deodorized butter passes through 2, 10 micron filters before being loaded into bulk tanker. Filters changed on a daily schedule or when pressure rises and indicated by system, which will shut down system.
Introduction of steam flash at deodorizing step, pulled out by vacuum to
reduce FFA, and reduction of flavor to cocoa butter. FFA removed to separate waste tank. Culinary filter inplace.
Incoming melted cocoa butter to be placed into a tank on the deodorized side of the facility to determine what is to
Be done with the incoming butter. If it is prime it will be placed into a prime tank, if deodorized butter to be placed in a
deodorized tank, if butter needs to be deodorized it can be brought into the melting side to be placed in a holding tank, see
Page 1. Inbound cocoa butter to deodorizing side will be filtered through a 10 micron filter coming into the facility. Then
shipped according to routine shipments as stated above.